## Slide 1: Computer Organization & Assembly Language (Lecture 13)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Stack
Stack is an area of memory for keeping temporary data/ addresses
Stack is used by:
  PUSH instruction to store the data
  POP instruction to get the data
  CALL instruction to store the return address of function/ procedure
  RET instruction to get the address and returns to that offset

## Slide 3: PUSH Instruction
  PUSH instruction stores 16-bit value in the stack
Syntax for PUSH instruction:
  PUSH REG
  PUSH SREG
  PUSH memory
  PUSH immediate
REG: AX, BX, CX, DX, DI, SI, BP, SP SREG: DS, ES, SS, CS memory: [BX], [BX+SI+7], 16 bit variable, etc... immediate: 5, -24, 3Fh, 10001101b, etc...

## Slide 4: POP Instruction
  POP instruction gets 16-bit value from the stack
Syntax for POP instruction:
  POP REG
  POP SREG
  POP memory
REG: AX, BX, CX, DX, DI, SI, BP, SP
SREG: DS, ES, SS (except CS)
memory: [BX], [BX+SI+7], 16 bit variable, etc...

## Slide 5: CALL Instruction
  CALL instruction stores 16-bit address of function/ procedure in the stack
  Syntax for CALL instruction:
  call Function_Name

## Slide 6: RET Instruction
  RET instruction gets 16-bit address from the stack and returns to that offset address
  Syntax for RET instruction:
  ret

## Slide 7
The stack uses FILO (First In, Last Out) or LIFO (Last In, First Out)
It is very important to do equal number of PUSHs and POPs, otherwise the stack may get corrupted and it will be impossible to return to the required address

## Slide 8
The stack memory area is set by SS (Stack Segment) register, and SP (Stack Pointer) register
Generally operating system sets values of these registers on program start
"PUSH source" instruction does the following:
  Subtract 2 from SP register
  Write the value of source to the address SS:SP

## Slide 9
"POP destination" instruction does the following:
  Write the value at the address SS:SP to destination
  Add 2 to SP register
The current address pointed by SS:SP is called top of the stack

## Slide 10: Example 01
Show the values of AX and Stack for all executable instructions
  [org 0x100]
  mov ax,0x1234
  push ax
  mov ax,0x1
  add ax,1
  pop ax
  mov ax,0x4C00
  int 0x21

## Slide 11: Solution
Syntax | AX | Stack
[org 0x100] |  | 
mov ax, 0x1234 | 1234 | 0000
push ax | 1234 | 1234
mov ax,0x1 | 0001 | 1234
add ax,1 | 0002 | 1234
pop ax | 1234 | 0000
mov ax, 0x4C00 |  | 
int 0x21 |  | 

## Slide 12: Task 01
Let, AX = 1234 and BX = 5678.
Swap the values of AX with BX using stack.

## Slide 13: Example 02
Show the values of AX, BX and Stack for all executable instructions
  [org 0x100]
  mov ax,2 ;100
  mov bx,3 ;103
  call addition ;106
  call addition ;109
  mov ax,0xFFFF ;10C
  mov ax,0x4C00 ;10F
  int 0x21 ; 112
  addition:
  add ax,bx ;114
  ret ;116

## Slide 14: Task 02
Show the values of AX, BX and Stack for all executable instructions
  [org 0x100]
  mov ax,2 ;100
  mov bx,3 ;103
  call addition ;106
  call addition ;109
  mov ax,0xFFFF ;10C
  mov ax,0x4C00 ;10F
  int 0x21 ; 112
  addition:
  push 3
  add ax,bx
  pop ax
  ret

## Slide 15: Example 03
Show the values of AX, BX and Stack for all executable instructions
  [org 0x100]
  mov ax,2 ;100
  mov bx,3 ;103
  call addition ;106
  mov ax,0xFFFF ;109
  mov ax,0x4C00 ;10C
  int 0x21 ;10F
  addition:
  add ax,bx ;111
  call subtraction ;113
  ret ;116
  subtraction:
  sub ax,2 ;117
  ret ;11A

## Slide 16: xchg Instruction
xchg stands for “Exchange”
xchg instruction is used to swap the value between either two registers, or one register and one memory location
Syntax:
  xchg ax, bx

## Slide 17: Example 04
Show the values of AX and memory for all executable instructions.
  [org 0x100]
  mov ax,2
  xchg ax, [Tag]
  mov ax,0x4C00
  int 0x21
  Tag: dw 5,6,7

## Slide 18: Solution
Syntax | AX
[org 0x100] | 
mov ax, 2 | 0002
xchg ax, [Tag] | 0005
mov ax, 0x4C00 | 
int 0x21 | 
Tag dw: 5,6,7 | 
Memory |  | 
05 00 | 06 00 | 07 00
02 00 | 06 00 | 07 00

## Slide 19: Task 03
Show the values of AX, BX and Stack for all executable instructions.
  [org 0x100]
  mov ax,2 ;100
  mov bx,1 ;103
  call function1 ;106
  mov ax,bx ;109
  add ax,1 ;10B
  sub bx,1 ;10E
  shl ax,1 ;112
  pop ax ;114
  mov ax,0x4C00 ;115
  int 0x21 ;118
  function1:
  add ax,bx ;11A
  push 0x112 ;11C
  ret ;11F

## Slide 20: Recap
SP (Stack Pointer)
  The 16-bit SP register is the stack pointer, used to manage push and pop operations
  It points to the top item of the stack
  It works with SS register (SS:SP)
BP (Base Pointer)
  The 16-bit BP register is the base pointer, mainly used to access parameters passed to the functions/ procedures
  It works with SS register (SS:BP)

## Slide 21: Function
A function is a block of organized, reusable code that is used to perform a single task or multiple tasks
All discussed with examples and class tasks

## Slide 22: Parameters vs. Arguments
Function Parameters are the names listed in the function's definition
Function Arguments are the real values passed to the function
Parameters are initialized to the values of the arguments supplied

## Slide 23: Parameter Passing through Stack
Consider the following piece of code:
  [org 0x100]
  push 3
  push 7
  call f1
  pop cx
  pop dx
  mov ax,0x4C00
  int 0x21
  f1:
  push bp
  mov bp,sp
  mov ax,[bp+6]
  mov bx,[bp+4]
  add ax,bx
  pop bp
  ret

## Slide 24: Task 04
Show the values of AX, BX and Stack for all executable instructions.
  [org 0x100]
  push 3
  push 7
  call f1
  mov ax,0x4C00
  int 0x21
  f1:
  push bp
  mov bp,sp
  mov ax,[bp+6]
  mov bx,[bp+4]
  add ax,bx
  pop bp
  ret 4

## Slide 25: Local Variables on Stack
A local variable is only accessible within a specific part of a program
These variables are usually local to a subroutine and are declared or defined within that routine
Local variable exists only till function invocation/ call and vanishes with the end of function execution

## Slide 26: Example 05
Show the values of AX, BX and Stack for all executable instructions.
  [org 0x100]
  push 3
  push 7
  call f1
  mov ax,0x4C00
  int 0x21
  f1:
  push bp
  mov bp,sp
  sub sp,2
  mov word[bp-2], 1
  mov ax,[bp+6]
  mov bx,[bp+4]
  add ax,bx
  mov sp,bp
  pop bp
  ret 4