## Slide 1: Computer Organization & Assembly Language (Lecture 14)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Display/ Video Memory
The debugger gives a very close vision of the processor, that is why every program written till now was executed inside the debugger (Advance Free Debugger (AFD))
We will now be using the display screen/ console screen to interact with the system/ hardware

## Slide 3
In order to interact with hardware, an Operating System (OS) is required
An OS is the software that controls a computer's hardware and peripheral devices and allows other software programs to function
As discussed in earlier lectures, 16-bit architecture supports up to 1 MB of memory

## Slide 4: Recap
Code Segment (CS)
  It contains all the instructions to be executed
  A 16-bit Code Segment Register or CS Register stores the starting address of the code segment
Data Segment (DS)
  It contains data
  A 16-bit Data Segment Register or DS Register stores the starting address of the data segment
Extra/ Extended Segment (ES)
  It is used to store data, incase the data segment is not sufficient to store all data
  A 16-bit Extra Segment Register or ES Register stores the starting address of the extra segment

## Slide 5
Consider 12F3:4B27 (Logical Address)
Put ‘o’ at the end of Base/ Segment Address and add it with Offset Address
1 2 F 3 o
0 4 B 2 7
1 7 A 5 7
12F3:4B27 corresponds to the physical address 0x17A57
Base/ Segment
Address
Offset Address
+
1

## Slide 6
Consider the following portion of RAM:
CS/ DS 1000
IP 1010
ES B800
The physical address of location pointed by IP will be 0x11010

## Slide 7
From memory address 0x0B800, 4000 bytes are reserved to be mapped on console screen
Total Cells: 80*25 = 2000
Each cell is of 2 bytes (MSB for attribute & LSB for character)
Standard screen size: (80*2)*25 = 4000 bytes
80 Cells
25 Rows
Console Screen

## Slide 8
B | RGB | I | RGB | ASCII Code
Cell Structure
Style Byte
Character Byte
0: On
1: Blink
0:Normal
1: Bold
Background Color
Foreground Color

## Slide 9
Whatever you write in these 2000 cells (4000 bytes), it will appear on screen
We will move ES register to B800, to access memory
To print out a black background color and white foreground color (code: 0x07) space character (code: 0x20) to the all cells on the screen consider the following example:

## Slide 10: Example 01
  [org 0x0100]
  mov ax, 0xb800 ;Video Memory Base
  mov es, ax
  mov di, 0 ;First Location
  Position:
  mov word [es:di], 0x0720
  ; 07: Black Background Color and White Foreground Color
  ; 20: Space Character
  add di, 2
  cmp di, 4000
  jne Position
  mov ax, 0x4c00
  int 0x21

## Slide 11: Task 01
Display white color ‘e’ character on all cells in console screen.
  ‘e’ Character ASCII code: 65
  Black Background Color and White Foreground Color ASCII code: 07

## Slide 12: Example 02
In example number 2, 24 out of 25 rows were visible, due to scroll function. All 25 row can be displayed using the following procedure
  [org 0x0100]
  mov ax, 0xb800 ;Video Memory Base
  mov es, ax
  mov di, 0 ;First Location
  Position:
  mov word [es:di], 0x0765
  ; 07: Black Background Color and White Foreground Color
  ; 65: Character ‘e’
  add di, 2
  cmp di, 4000
  jne Position
  ; wait for keypress
  mov ah, 0x1
  int 0x21
  mov ax, 0x4c00
  int 0x21

## Slide 13: Example 03
  [org 0x0100]
  mov ax, message
  push ax
  push word [length]
  call printstring
  mov ah, 0x1
  ; wait for keypress
  int 0x21
  mov ax, 0x4c00
  int 0x21
  printstring:
  push bp
  mov bp, sp
  push es
  push ax
  push cx
  push si
  push di
  mov ax, 0xb800
  mov es, ax
  mov di, 0
  mov si, [bp + 6]
  mov cx, [bp + 4]
  mov ah, 0x07
  nextchar:
  mov al, [si]
  mov [es:di], ax
  add di, 2
  add si, 1
  loop nextchar
  pop di
  pop si
  pop cx
  pop ax
  pop es
  pop bp
  ret 4
  message: db 'hello world'
  length: dw 11
Print “Hello World” in console screen.

## Slide 14: Example 04
  [org 0x0100]
  call clearscreen
  mov ax, message
  push ax
  push word [length]
  call printstring
  mov ah, 0x1
  ; wait for keypress
  int 0x21
  mov ax, 0x4c00
  int 0x21
  clearscreen:
  push es
  push ax
  push di
  mov ax, 0xb800
  mov es, ax
  mov di, 0
  nextloc:
  mov word [es:di], 0x0720
  add di, 2
  cmp di, 4000
  jne nextloc
  pop di
  pop ax
  pop es
  ret
  printstring:
  push bp
  mov bp, sp
  push es
  push ax
  push cx
  push si
  push di
  mov ax, 0xb800
  mov es, ax
  mov di, 0
  mov si, [bp + 6]
  mov cx, [bp + 4]
  mov ah, 0x07 ; only need to do this once
  nextchar:
  mov al, [si]
  mov [es:di], ax
  add di, 2
  add si, 1
  loop nextchar
  pop di
  pop si
  pop cx
  pop ax
  pop es
  pop bp
  ret 4
  message: db 'hello world'
  length: dw 11
First clear screen and then print “Hello World”.

## Slide 15: Example 05
  [org 0x0100]
  call clearscreen
  mov ax, 12
  push ax
  call printnumber
  mov ah, 0x1
  int 0x21
  mov ax, 0x4c00
  int 0x21
  clearscreen:
  push es
  push ax
  push di
  mov ax, 0xb800
  mov es, ax
  mov di, 0
  nextloc:
  mov word [es:di], 0x0720
  add di, 2
  cmp di, 4000
  jne nextloc
  pop di
  pop ax
  pop es
  ret
  printnumber:
  push bp
  mov bp, sp
  push es
  push ax
  push bx
  push cx
  push dx
  push di
  ; Number Splitting
  mov ax, [bp+4] ; number to print
  mov bx, 10
  mov cx, 0
  nextdigit:
  mov dx, 0 ; zero out
  div bx
  add dl, 0x30 ; convert to ASCII
  push dx
  inc cx
  cmp ax, 0 ; is there something in quotient?
  jnz nextdigit
  ; Printing
  mov ax, 0xb800
  mov es, ax
  mov di, 0
  nextpos:
  pop dx ; digit to output
  mov dh, 0x07
  mov [es:di], dx
  add di, 2
  loop nextpos
  pop di
  pop dx
  pop cx
  pop bx
  pop ax
  pop es
  pop bp
  ret 2
Print Number ‘12’ in console screen.

## Slide 16: Example 06
Print character ‘a’ in console screen using Interrupt.
  [org 0x100]
  mov dl,'a'
  mov ah,0x2
  int 0x21
  mov ax,0x4C00
  int 0x21

## Slide 17: Example 07
Print ‘Hello World’ in console screen using Interrupt.
  [org 0x100]
  mov dl,STRING
  mov ah,0x9
  int 0x21
  mov ax,0x4C00
  int 0x21
  STRING DB 'Hello World', '$'