## Slide 1: Computer Organization & Assembly Language (Lecture 08)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Jump Instructions

## Slide 3: Jump Instructions
Jump Instructions are used for changing the flow of execution of instructions in the processor
There are two types of Jump instructions:
  Unconditional Jump Instructions
  Conditional Jump Instructions

## Slide 4: Unconditional Jump Instructions
These instructions are used to jump on a particular location unconditionally, i.e. there is no need to satisfy any condition for the jump to take place
Syntax:
  jmp tag

## Slide 5: Example
Show the values of AX and BX for all executable instructions.
  [org 0x0100]
  mov ax,0x4D2
  mov bx,0x38
  add bh,al
  jmp tag1
  jmp tag2
  sub ah,0xFF
  tag1:
  mov ax,0
  tag2:
  add ax,0xFFFF
  mov ax,0x4c00
  int 0x21

## Slide 6: Solution
Syntax | AX |  | BX | 
 | AH | AL | BH | BL
[org 0x100] |  |  |  | 
Mov ax, 1234 | 04 | D2 | 00 | 00
Mov bx, 56 | 04 | D2 | 00 | 38
Add bh,al | 04 | D2 | D2 | 38
Jmp Tag1 | 04 | D2 | D2 | 38
Jmp Tag2 |  |  |  | 
Sub ah, 0FFH |  |  |  | 
Tag1: |  |  |  | 
Mov ax, 0 | 00 | 00 | D2 | 38
Tag2: |  |  |  | 
Add ax, 0FFFFH | FF | FF | D2 | 38
Ret |  |  |  | 

## Slide 7: Task 01
Show the values of AX and BX for all executable instructions.
  [org 0x0100]
  mov ax,0x4D2
  mov bx,0x38
  add bh,al
  jmp tag1
  jmp tag2
  sub ah,0xFF
  tag1:
  mov ax,0
  mov ax,0x4c00
  int 0x21
  tag2:
  add ax,0xFFFF
  mov ax,0x4c00
  int 0x21

## Slide 8: Task 02
Show the values of AX and BX for all executable instructions.
  [org 0x0100]
  mov ax,1
  mov bx,5
  jmp tag3
  add bh,al
  jmp tag1
  jmp tag2
  sub ah,0xFF
  tag1:
  mov ax,0
  tag3:
  tag2:
  add ax,0xFFFF
  mov ax,0x4c00
  int 0x21

## Slide 9: Conditional Jump Instruction
In these types of instructions, the processor must check for the particular condition. If it is true, only then jump takes place, else the normal flow of program execution is maintained
The arithmetic and logic operations set flags
The conditional jump statements test the flags and jump if the relevant flag is set

## Slide 10
Conditional jump instructions are as follows:
  JE / JZ
  JNE / JNZ
  JC / JB
  JNC / JNB
  JS
  JNS
  JO
  JNO
  JP / JPE
  JNP / JPO

## Slide 11: JE / JZ
JE stands for ‘Jump if Equal’
JZ stands for ‘Jump if Zero’
It checks whether the Zero Flag is set or not
  If ZF = 1, then jump
  Else, do nothing

## Slide 12: JNE / JNZ
JNE stands for ‘Jump if Not Equal’
JNZ stands for ‘Jump if Not Zero’
It checks whether the Zero Flag is set or not
  If ZF = 0, then jump
  Else, do nothing

## Slide 13: JC / JB
JC stands for ‘Jump if Carry’
JB stands for ‘Jump if Below’
It checks whether the Carry Flag is set or not
  If CF = 1, then jump
  Else, do nothing

## Slide 14: JNC / JNB
JNC stands for ‘Jump if Not Carry’
JNB stands for ‘Jump if Not Below’
It checks whether the Carry Flag is set or not
  If CF = 0, then jump
  Else, do nothing

## Slide 15: JS
JS stands for ‘Jump if Sign’
It checks whether the Sign Flag is set or not
  If SF = 1, then jump
  Else, do nothing

## Slide 16: JNS
JNS stands for ‘Jump if Not Sign’
It checks whether the Sign Flag is set or not
  If SF = 0, then jump
  Else, do nothing

## Slide 17: JO
JO stands for ‘Jump if Overflow’
It checks whether the Overflow Flag is set or not
  If OF = 1, then jump
  Else, do nothing

## Slide 18: JNO
JNO stands for ‘Jump if Not Overflow’
It checks whether the Overflow Flag is set or not
  If OF = 0, then jump
  Else, do nothing

## Slide 19: JP / JPE
JP stands for ‘Jump if Parity’
JPE stands for ‘Jump if Even Parity’
It checks whether the Parity Flag is set or not
  If PF = 1, then jump
  Else, do nothing

## Slide 20: JNP / JPO
JNP stands for ‘Jump if Not Parity’
JPO stands for ‘Jump if Odd Parity’
It checks whether the Parity Flag is set or not
  If PF = 0, then jump
  Else, do nothing

## Slide 21
Conditional jump instructions for Signed Numbers are as follows:
  JG / JNLE
  JNG / JLE
  JL / JNGE
  JNL / JGE

## Slide 22: JG / JNLE
JG stands for ‘Jump if Greater’
JNLE stands for ‘Jump if Not Less or Equal’
  If ZF = 0 and SF = OF, then jump
  Else, do nothing

## Slide 23: JNG / JLE
JNG stands for ‘Jump if Not Greater’
JLE stands for ‘Jump if Less or Equal’
  If ZF = 1 and SF != OF, then jump
  Else, do nothing

## Slide 24: JL / JNGE
JL stands for ‘Jump if Less’
JNGE stands for ‘Jump if Not Greater or Equal’
  If SF != OF, then jump
  Else, do nothing

## Slide 25: JNL / JGE
JNL stands for ‘Jump if Not Less’
JGE stands for ‘Jump if Greater or Equal’
  If SF = OF, then jump
  Else, do nothing

## Slide 26
Conditional jump instructions for Un-signed Numbers are as follows:
  JA / JNBE
  JNA / JBE
  JB / JNAE
  JNB / JAE

## Slide 27: JA / JNBE
JA stands for ‘Jump if Above’
JNBE stands for ‘Jump if Not Below or Equal’
  If CF = 0 and ZF = 0, then jump
  Else, do nothing

## Slide 28: JNA / JBE
JNA stands for ‘Jump if Not Above’
JBE stands for ‘Jump if Below or Equal’
  If CF = 1 and ZF = 1, then jump
  Else, do nothing

## Slide 29: JB / JNAE
JB stands for ‘Jump if Below’
JNAE stands for ‘Jump if Not Above or Equal’
  If CF = 1, then jump
  Else, do nothing

## Slide 30: JNB / JAE
JNB stands for ‘Jump if Not Below’
JAE stands for ‘Jump if Above or Equal’
  If CF = 0, then jump
  Else, do nothing

## Slide 31: Example
Show the values of AX, BX, ZF, OF, SF, AF, PF and CF for all executable instructions.
  [org 0x0100]
  mov al,2
  mov bl,2
  cmp al,bl
  jne Tag2
  je Tag1
  jmp Tag2
  Tag1:
  add al, 0FFH
  jnc Tag2
  jc Tag3
  mov ax,0x4c00
  int 0x21
  Tag2:
  sub al,bl
  mov ax,0x4c00
  int 0x21
  Tag3:
  mov ax, 0
  mov ax,0x4c00
  int 0x21

## Slide 32: Solution
Syntax | AX |  | BX |  | ZF | OF | SF | AF | PF | CF | IF
 | AH | AL | BH | BL |  |  |  |  |  |  | 
Org 100h |  |  |  |  |  |  |  |  |  |  | 
Mov al, 2 | 00 | 02 | 00 | 00 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Mov bl, 2 | 00 | 02 | 00 | 02 | 0 | 0 | 0 | 0 | 0 | 0 | 1
cmp al, bl | 00 | 02 | 00 | 02 | 1 | 0 | 0 | 0 | 1 | 0 | 1
Jne Tag2 | 00 | 02 | 00 | 02 | 1 | 0 | 0 | 0 | 1 | 0 | 1
Je Tag1 | 00 | 02 | 00 | 02 | 1 | 0 | 0 | 0 | 1 | 0 | 1
Jmp Tag2 |  |  |  |  |  |  |  |  |  |  | 
Tag1: |  |  |  |  |  |  |  |  |  |  | 
Add al, 0FFH | 00 | 01 | 00 | 02 | 0 | 0 | 0 | 1 | 0 | 1 | 1

## Slide 33
Syntax | AX |  | BX |  | ZF | OF | SF | AF | PF | CF | IF
 | AH | AL | BH | BL |  |  |  |  |  |  | 
Jnc Tag2 | 00 | 01 | 00 | 02 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Jc Tag3 | 00 | 01 | 00 | 02 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Ret |  |  |  |  |  |  |  |  |  |  | 
Tag2: |  |  |  |  |  |  |  |  |  |  | 
Sub al,bl |  |  |  |  |  |  |  |  |  |  | 
Ret |  |  |  |  |  |  |  |  |  |  | 
Tag3: |  |  |  |  |  |  |  |  |  |  | 
Mov ax, 0 | 00 | 00 | 00 | 02 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Ret |  |  |  |  |  |  |  |  |  |  | 

## Slide 34: Task 03
Show the values of AX, BX, ZF, OF, SF, AF, PF and CF for all executable instructions.
  [org 0x0100]
  mov al,0x80
  mov bl,0x4
  add al,bl
  jg Tag1
  ja Tag2
  jl Tag3
  jb Tag4
  Tag1:
  mov ax,0x1111
  mov ax,0x4c00
  int 0x21
  Tag2:
  mov ax,0x2222
  mov ax,0x4c00
  int 0x21
  Tag3:
  mov ax,0x3333
  mov ax,0x4c00
  int 0x21
  Tag4:
  mov ax,0x4444
  mov ax,0x4c00
  int 0x21

## Slide 35: Task 04
Show the values of AX, BX, ZF, OF, SF, AF, PF and CF for all executable instructions.
  [org 0x0100]
  mov al,0x80
  mov bl,0x4
  sub al,bl
  jg Tag1
  ja Tag2
  jl Tag3
  jb Tag4
  Tag1:
  mov ax,0x1111
  mov ax,0x4c00
  int 0x21
  Tag2:
  mov ax,0x2222
  mov ax,0x4c00
  int 0x21
  Tag3:
  mov ax,0x3333
  mov ax,0x4c00
  int 0x21
  Tag4:
  mov ax,0x4444
  mov ax,0x4c00
  int 0x21