## Slide 1: Computer Organization & Assembly Language (Lecture 09)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Unconditional Loops
Instruction | Condition(s)
loop tag | CX != 0

## Slide 3: Conditional Loops
Instruction | Condition(s)
loope tag | CX != 0 & ZF = 1
loopz tag | CX != 0 & ZF = 1
loopne tag | CX != 0 & ZF = 0
loopnz tag | CX != 0 & ZF = 0

## Slide 4: Unconditional Jumps
Instruction | Condition(s)
jmp tag | --

## Slide 5: Conditional Jumps
Instruction | Condition(s)
je | ZF = 1
jne | ZF = 0
jz | ZF = 1
jnz | ZF = 0
jc | CF = 1
jnc | CF = 0
js | SF = 1
jns | SF = 0
jo | OF = 1
jno | OF = 0

## Slide 6
Instruction | Condition(s)
jp | PF = 1
jnp | PF = 0
jg | ZF = 0 & SF = OF
jng | ZF = 1 & SF != OF
jl | SF != OF
jnl | SF = OF
ja | CF = 0 & ZF = 0
jna | CF = 1 & ZF = 1
jb | CF = 1
jnb | CF = 0

## Slide 7: Jump vs. Loop Instructions

## Slide 8: Comparison
Consider the following piece of codes:
  [org 0x0100]
  mov ax,0
  mov bx,1
  mov cx,5
  tag1:
  add ax,bx
  loop tag1
  mov ax,0x4c00
  int 0x21
  [org 0x0100]
  mov ax,0
  mov bx,1
  mov cx,5
  tag1:
  add ax,bx
  sub cx,1
  jne tag1
  mov ax,0x4c00
  int 0x21

## Slide 9: Task 01
Modify the given piece of code using conditional loop(s) along with conditional jump(s) such that the output remains same.
  [org 0x0100]
  mov ax,2
  mov bx,2
  mov cx,10
  tag1:
  mul bx
  sub cx,1
  cmp ax,cx
  jne tag1
  mov ax,0x4c00
  int 0x21

## Slide 10: Task 02
Convert the given piece of code using conditional jump(s) such that the output remains same.
  [org 0x0100]
  mov ax,2
  mov bx,2
  mov cx,4
  tag1:
  add ax,2
  sub ax,bx
  loop tag1
  mov ax,0x4c00
  int 0x21

## Slide 11: Task 03
Develop an assembly language program utilizing conditional/ unconditional jumps/ loops, such that it can print the following series without utilizing CX/ CH/ CL register:
1 2 4 8 10
The given series is in hexadecimal number system