## Slide 1: Computer Organization & Assembly Language (Lecture 10)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Content
x86 Architecture Details
  Modes of Operation

## Slide 3: Modes of Operations
x86 processors have three primary modes of operation:
  Real Address Mode
  Protected Mode
    A sub-mode, named Virtual-8086, is a special case of Protected Mode
  System Management Mode

## Slide 4
Logical Address or Virtual Address
  An address generated by the CPU
Physical Address
  An address actually available on memory unit

## Slide 5: Real Mode
Real Mode, also known as Real Address Mode, is an operating mode of all x86 compatible CPUs
Real Mode gives an unlimited direct software access to all addressable memory, I/O addresses and peripheral hardware
Real Mode provides no support for memory protection, multitasking or code privilege levels

## Slide 6
Before the release of the 80386, which introduced Protected Mode, Real Mode was the only available mode for x86 CPUs
In the interest of backwards compatibility, all x86 CPUs start in real mode when reset
Processor 8086 works in Real Mode
Real Mode is characterized by a 20 bit segmented memory address space (giving exactly 1 MB of addressable memory)

## Slide 7: Protected Mode
Protected Mode is the native state of the processor, in which all instructions and features are available
Programs are given separate memory areas named segments and the processor prevents programs from referencing memory outside their assigned segments
Protected Mode provides support for memory protection, multitasking and code privilege levels

## Slide 8
Protected Mode was introduced in 80386 Intel processor
Protected mode in 80386 was characterized by a 32 bit segmented memory address space
  access up to 2^32 bytes = 4 GB Memory Size
Physical address in protected mode is calculated as:
Virtual Address Physical Address
The idea behind paging is that we split a process's logical address space into many small chunks called pages
Paging

## Slide 9
The mapping from virtual to physical address is done by the memory management unit (MMU) which is a hardware device and this mapping is known as paging technique
The Physical Address Space is conceptually divided into a number of fixed-size blocks, called frames
The Logical address Space is also divided into fixed-size blocks, called pages
Page Size = Frame Size

## Slide 10: Virtual 8086 Mode
Virtual 8086 Mode (also called Virtual Real Mode, V86-Mode or VM86) allows the execution of Real Mode applications while the processor is running a Protected Mode operating system

## Slide 11: System Management Mode
System Management Mode (SMM) is an operating mode of x86 in which all normal execution, including the operating system, is suspended and special separate software, which is usually a part of the firmware or a hardware-assisted debugger, is executed with high privileges

## Slide 12
Some uses of the System Management Mode are:
  Handle system events like memory or chipset errors
  Manage system safety functions, such as shutdown on high CPU temperature and turning the fans ON and OFF
  Sleep power management support on Intel systems