## Slide 1: Computer Organization & Assembly Language (Lecture 11)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: Task 01
What will be the difference between the outputs of following code:
  [org 0x0100]
  mov ax,0
  mov bx,0
  Label1:
  add ax,[Tag1+bx]
  add bx,2
  cmp bx,8
  jne Label1
  mov ax,0x4c00
  int 0x21
  Tag1: dw 10, 11, 12, 13
  [org 0x0100]
  Tag1: dw 10, 11, 12, 13
  mov ax,0
  mov bx,0
  Label1:
  add ax,[Tag1+bx]
  add bx,2
  cmp bx,8
  jne Label1
  mov ax,0x4c00
  int 0x21

## Slide 3: Sorting
Sorting means to arrange data/ things in an order according to their kind, class or nature
Order can be ascending or descending
  Ascending
    1, 2, 3 , 4
  Descending
    4, 3, 2, 1

## Slide 4: Sorting Algorithm: Ascending
Let, we have ‘n’ numbers, say A1, A2, A3, . . ., An
Compare first 2 numbers, say A1 and A2
  If A2 < A1, then swap A1 with A2
  Else, do nothing
Then compare next 2 numbers (say updated A2 and A3) and apply the same condition statements as discussed above
Repeat the same procedure untill you reach An
Repeat the whole procedure untill the data is sorted

## Slide 5: Sorting Algorithm: Descending
Let, we have ‘n’ numbers, say A1, A2, A3, . . ., An
Compare first 2 numbers, say A1 and A2
  If A2 > A1, then swap A1 with A2
  Else, do nothing
Then compare next 2 numbers (say updated A2 and A3) and apply the same condition statements as discussed above
Repeat the same procedure untill you reach An
Repeat the whole procedure untill the data is sorted

## Slide 6: Scenario 01
  [org 0x0100]
  mov cx, 4
  outerloop:
  mov bx,0
  innerloop:
  mov ax,[data+bx]
  cmp ax ,[data+bx+2]
  jna donothing
  mov dx, [data+bx+2]
  mov [data+bx+2], ax
  mov [data+bx], dx
  donothing:
  add bx,2
  cmp bx,6
  jne innerloop
  loop outerloop
  mov ax,0x4c00
  int 0x21
  data: dw 6, 4, 5, 2

## Slide 7: Scenario 02
  [org 0x0100]
  mov cx, 4
  outerloop:
  mov bx,0
  innerloop:
  mov ax,[data+bx]
  cmp ax ,[data+bx+2]
  jna donothing
  mov dx, [data+bx+2]
  mov [data+bx+2], ax
  mov [data+bx], dx
  mov byte [swap], 1
  donothing:
  mov byte [swap],0
  add bx,2
  cmp bx,6
  jne innerloop
  cmp byte [swap], 0
  je exit
  loop outerloop
  exit:
  mov ax,0x4c00
  int 0x21
  data: dw 6, 2, 4, 5
  swap: db 0

## Slide 8: Task 02
Sort the following data is desceneding order:
1, 3, 2, 4, 5