## Slide 1: Computer Organization & Assembly Language (Lecture 16)
Omar Bin Samin
Lecturer
Institute of Management Sciences, Peshawar.

## Slide 2: String
A string is a sequence of characters (including spaces) enclosed in single or double quotes:
  'ABC'
  "Hello"
  '4096'
Embedded quotes are permitted when used in the manner shown as follows:
  "This isn't a test"
  ' "Pakistan" is a free country'

## Slide 3: Example 01
Consider the following program for printing “e”.
  [org 0x0100]
  mov cx,2000
  mov ax, 0xb800
  mov es, ax
  mov di, 0 ;First Location
  Position:
  mov word [es:di], 0x0765
  add di, 2
  loop Position
  mov ax, 0x4C00
  int 0x21

## Slide 4
The use of loops in Example 01 may result in:
  Bugs
  Slow processing
This issue is typically faced when using Strings
These issues can be addressed and resolved using “String Instructions”

## Slide 5: String Instructions
Commonly used string instructions are as follows:
  STOS: Store string
  LODS: Load string
  CMPS: Compare string
  SCAS: Scan string
  MOVS: Move string

## Slide 6
Each of these instructions has two variants:
  A byte variant
  A word variant
The variant can be obtained by appending a B or W at the end of the instruction
  STOSB
  STOSW
The variant determines, how the offsets (DI and SI) will be incremented/decremented

## Slide 7: STOS
STOS stands for “Store String”
STOS transfers a byte or word from the register AL or AX to the memory element addressed by (ES:DI) and updates DI to the next location

## Slide 8: LODS
LODS stands for “Load String”
LODS transfers a byte or word from the source location (DS: SI) to AL or AX

## Slide 9: CMPS
CMPS stands for “Compare String”
CMPS subtracts the source location DS: SI from the destination location ES: DI without affecting the source and destination themselves
SI and DI are updated accordingly

## Slide 10: SCAS
SCAS stands for “Scan String”
SCAS compares a source byte or word in register AL or AX with the destination string element addressed by ES:DI and updates the flags
SCAS is used to check equality/ inequality in a string using REPE or REPNE

## Slide 11: MOVS
MOVS stands for “Move String”
MOVS transfers a byte or word from DS: SI to ES: DI and updates SI and DI accordingly
It is used to move a block of memory

## Slide 12
Whenever an instruction needs a memory source, DS:SI holds a pointer to it
For the memory destination, the pointer is placed in ES:DI
  DS: Data Segment
  ES: Extended Segment
  SI: Source Index
  DI: Destination index

## Slide 13
REP (Repeat)
REPNE (Repeat Not Equal)

## Slide 14: Recap
Direction flag (DF) is specifically used in string instructions
If directional flag is set (1), then access the string data from higher memory location towards lower memory location (Reverse Direction)
  Syntax: STD
If directional flag is reset (0), then access the string data from lower memory location towards higher memory location (Forward Direction)
  Syntax: CLD

## Slide 15
STD (Set Direction Flag)
  Auto decrement
  Initially DI = 2000
  DI--
CLD (Clear Direction flag)
  Auto increment
  Initially DI = 0
  DI++

## Slide 16: Example 02
Consider the following program for printing “e” using String Instruction.
  [org 0x0100]
  mov ax, 0xb800
  mov es, ax
  mov di, 0 ;First Location
  mov ax, 0x0765
  mov cx,2000
  cld
  rep stosw ; rep cx times, store words
  ; source is ax for word, al for bytes
  ; destination is es:di
  ; inc/dec di as well by 2 bytes
  mov ax, 0x4C00
  int 0x21